## Slide 1: Do Now Task
Log in and Open
Log in and Open chrome
Search
Search for BBC Make Code
Create
Create a new project called : Temp
Using
Using the computer as required, answer the questions in the do now task section.

## Slide 2: Make a Physical Microbit Game
Final Topic Project

## Slide 3: Do now questions : Answers
A pin can be either an input or a output for data.
A named container for information (the information inside this container can be read, replaced or changed hence … its variable)
Repetition …Loops!

## Slide 4: Do now questions : Answers
If statement! It’s a form of selection.
The type of information / data that a variable will contain.
String
Integer
Boolean

## Slide 5: Project Goals
Create a simple goal game using a Microbit.
Be introduced to your end of topic project.
Plan, create and program a functioning physical game using a Microbit.

## Slide 6: Basic Goal Game
Creating a simple tabletop football game

## Slide 7: Basic Goal Game - The Plan
We are going to create a basic ball game.
The game will consist of:
A goal made from carboard with to strips of foil running in it.
A Microbit that keeps scores of goals
A ball made from a rolled-up bit of foil.

## Slide 8: Basic Goal Game - The Plan
How the game will work:
  You flick the ball at the goal.
  If it goes in and makes a good connection the Microbit will count it as a goal.

## Slide 9: What you will need
Small piece of carboard.
A glue stick
A pair scissors
Some foil
Microbit and 2 crocodile clips.

## Slide 10: Method for making…

## Slide 11: Construction Method
First get your carboard piece and fold it in about half

## Slide 12: Construction Method
Next cut a small line across one side of the fold. Say around 2cm long (the red line)
Then fold the two edges so that they overlap. This is so the goal will stand up.

## Slide 13: Construction Method
Glue the overlap so that the goal will stand up on its own.

## Slide 14: Construction Method
Cut two 1cm(ish) wide strips of foil.
Attach the strips along the length of the goal.
Make sure that they are not touching!! But they need to be close.

## Slide 15: Construction Method
Attach a crocodile clips to each bit of foil. (it doesn’t matter the colour).
Attach one clip to pin 0 on the Microbit and the other to GND (ground).
Make a small ball from some foil.

## Slide 16: What you should now have.
A goal, a ball and the Microbit connected.

## Slide 17: Programming your Basic Goal Game
You will need to use:
  Variable section
  Basic section
  Input section
Task : What does this script do?

## Slide 18: Test & Review your Basic Goal Game
Does it work?
Could it be improved?
Review the game on page 4.

## Slide 19: Your Challenge
Plan, Construct and Play!

## Slide 20: Your challenge.
You have the remaining time this term to construct something using the microbats.
It could be a physical game such as the one you have just created, something using the LED traffic lights or something using the Microbit alone.
    You might want to compose some music.
    Work with someone else so that it can send messages remotely.
    Or develop a more advanced version of rock paper scissors.
Its your time, your project but you need to create something!

## Slide 21: Your Plan
You will need to create a plan.
On page 5 create a mind map exploring ideas of what you will create using the remaining time.
Note: This will help you make your final project! DON’T SKIP THIS STAGE!

## Slide 22: Task: What is your project?
On page 6, set your self some goals for your final project.

## Slide 23: Task: What is the code for your game?
Now that you have created your project. What is the code for your final creation?

## Slide 24: Page 7: The Review
What went well?
Even better if?